Study and Investigations of RCM Methodology in Manufacturing Industry to Minimize Breakdown Maintenance

- P. Dawane1, Dr. C. M. Sedani2

1PG Scholar

Matsyodari Shikshan Santha’s, College of Engineering & Technology, Jalna, India, 431203

2Principal

Matsyodari Shikshan Santha’s, College of Engineering & Technology, Jalna, India, 431203

Abstract – The objective of the work is to improve the preventive maintenance schedule, increase the avaibility of machines, saving of total down time & production cost as compared to the current maintenance. The work is carried out in the industry manufacturing the parts of the refrigeration & air-conditions, where the operations like spinning, cutting to appropriate length, shaping & testing of these part are performed. The work is planned initially to find the all breakdown occurred with their frequency of occurrence, after that it is analyzed by the tools FMEA.This helps to develop and improve a new preventive maintenance checklist for the machines. This method is used to prevent the failure of equipment before it actually occurs. The work is finally leads to reducing sudden breakdown and increasing availability machines. This has been achieved by optimal utilization of time for maintenance, inspection frequency by considering manufacturer recommendation and previous experience. By all these procedures the availability of the machine will increases to a certain extent and also increases the production capacity, minimizes the maintenance cost and Reduces the down time.

Keywords- Breakdown, Down Time (DT), Preventive Maintenance (PM),

INTRODUCTION

Maintenance is generally identified as a single largest controllable cost and status quo represents a challenge for leading managements to re-evaluate their maintenance strategies, decision making work attempts to understand different maintenance policies making for better maintenance of asset.

The definition of maintenance often stated maintenance as an activity carried out for any equipment to ensure its reliability to perform its functions. Breakdown maintenance is one of the earliest maintenance programs being implemented in the industry. The approach to maintenance is totally reactive and only act when the equipment needs to be fixed. This strategy has no routine maintenance task and also described as no scheduled maintenance strategy. To rectify the problem, corrective maintenance is performed onto the equipment. Thus, this activity May consist of repairing, restoration or replacement of components.

RCM is a systematic approach to determine the maintenance requirements of plant and equipment in its

Operating. It is used to optimize preventive maintenance

(PM) strategies.

The developed PM programs minimize equipment failures and provide industrial plants with effective equipment. RCM is one of the best known and most used devices to preserve the operational efficiency of the system.

RCM philosophy employs preventive maintenance, predictive maintenance (PdM), real-time monitoring (RTM), run-to-failure (RTF) and proactive maintenance

Techniques is an integrated manner to increase the probability that a machine or component will function in the required manner over its design life cycle with a minimum of maintenance.

This work focused on causes of failure of machine by Tribological aspects, associated remedial action and accordingly generates a maintenance model that based on the RCM technique and preventive methodology rather condition based maintenance, for the worked manufacturing industry. This technique should be able to minimize the downtime (DT) and improve the improve the availability of the plant components. Also, it should benefits to decrease the spare parts consumption.

PROBLEM INDENTIFICATION

Production may be stopped due to many reasons like breakdown of machine, maintenance work, labor problem, insufficient material supply, problems in the method of production and many more.

Excluding all other factors like materials, method, man, measurements, it is necessary to reduce the breakdown of the machine or equipment’s in the industry for the efficient nonstop production to meet the demands.

Breakdowns are the most common causes of efficiency and production loss in manufacturing. Eliminating unplanned down time are critical to improving Overall Equipment Efficiency. It is not only important to know how much down time your process is experiencing (and when) but also to be able to attribute the lost time to the specific source or reason for the loss. Work was conducted on the breakdowns of machines or equipment’s of the industry and to find out the root causes of these breakdown so as to eliminate them and to decrease the downtime caused due to these.

WORK METHODOLOGY

This work was carried out in manufacturing unit located in the Jalna MIDC manufacturing the parts of refrigeration & air-conditioning by automated machines like CNC spinning, end forming machine, cut length machine & some manually operated machine like manual bending machine. All produced parts are gone through the leak testing machines.

- Data Collection

- Data Analysis

- FMEA

- Preventive Maintenance Check List

Initially failure mode, reason of failure from man, material machine, measurement and method, frequency of breakdown occurrence has been collected and according to this failure a proper maintenance strategy to reduce down time (DT), idle time and improvement in the overall equipment effectiveness (OEE) is increased and finally a proper preventive maintenance checklist have been designed for the worked industry.

DATA COLLECTION

Data Collection is an important aspect of any type of research study. Inaccurate data collection can impact the results of a study and ultimately lead to invalid results. Data is essential for investigating the Root Cause of the problem.

Failure Data Collection: The following information is collected as per the discussion with maintenance people and from the maintenance log books or sheets,

- The data about the causes of breakdown

- Breakdown hours

- Repair time, inspection time and maintenance action taken

- Parts replaced the data should also include the failure reasons related to machine, material, process, environment etc.

Data collection includes the probable causes of breakdown in all machines in the plant with their frequency of failures for the machines like CTL, CNC Spinning, End shaping machine etc., as all these machines having the same elements like hydraulic, pneumatic system it’s conveying part, electrical motors controlling panels, different controlling elements, FRL unit, pump bearings etc. and the breakdown occurred in these components effect more. For the down time, idle time, lost in production & increase in the associate cost. The breakdown data was collected for last six month from January-2016 to June-2016 from the maintenance log book & from the discussion with maintenance people & operator; it is tabulated as per following,

Table-1- Breakdown & its Occurrence Frequency

| Sr. No | Breakdown | Frequency |
| --- | --- | --- |
| 1 | Disturbances in Sensor setting | 27 |
| 2 | Handle pressure down | 25 |
| 3 | Lower the Pneumatic pressure | 25 |
| 4 | Lower Clamping Pressure | 22 |
| 5 | Cutting length variation in CTL | 17 |
| 6 | Oil leakage through guider | 17 |
| 7 | Guider Screw not working | 16 |
| 8 | Strippers becomes loose | 15 |
| 9 | Stoppers not properly working | 15 |
| 10 | Cutter wear down earlier | 11 |
| 11 | Clamping/decamping Pedal not working | 11 |
| 12 | Failure of hydraulic system | 11 |
| 13 | Spindle Speed goes down | 7 |
| 14 | Contamination in Filter | 7 |
| 15 | Sealing agents wear, stretched, loosed | 5 |
| 16 | Belt slippage, cracked, frayed, | 4 |
| 17 | Electrical Controllers Failed to receive or send feedbacks | 3 |
| 18 | Failure of gear train | 2 |
| 19 | Bearing Failures | 1 |
| 20 | Failure of Electrical system (Misalignment, Imbalance, looseness) | 1 |

DATA ANALYSIS

Collected data is analyzed by the following tools,

- Breakdown & Time Required to Recover

- Pie Chart for Time Required to Breakdown Recover

- FMEA

Fig.1. Pie Chart of Frequency of Occurrence

From the data collected it is clear that, disturbances in sensor setting (27) accounts for the most of the breakdown causing production loss to the company. Handle pressure down (25) lower the pneumatic pressure (25) etc. are other major breakdowns in the industry. Above failure occurrence is maximum but when seen it found that, it’s recover time is minimum, hence the sensor setting disturbances, handle pressure lower etc. Does not consume more time more to repair, hence causes less for breakdown of machines, 2 as per the data collected, times spend for getting back the equipment,

Table-2- Time Spend for Recover the components

| Sr. No | Breakdown | Time Spend (Min.) |
| --- | --- | --- |
| 1 | Disturbances in Sensor setting | 10 |
| 2 | Handle pressure down | 15 |
| 3 | Lower the Pneumatic pressure | 40 |
| 4 | Lower Clamping Pressure | 22 |
| 5 | Cutting length variation in CTL | 12 |
| 6 | Oil leakage through guider | 12 |
| 7 | Guider Screw not working | 17 |
| 8 | Strippers becomes loose | 5 |
| 9 | Stoppers not properly working | 11 |
| 10 | Cutter wear down earlier | 5 |
| 11 | Clamping/decamping Pedal not working | 15 |
| 12 | Failure of hydraulic system components | 70 |
| 13 | Spindle Speed goes down | 40 |
| 14 | Contamination in Filter | 30 |
| 15 | Sealing agents wear, stretched loosed | 20 |
| 16 | Belt slippage, cracked, frayed | 20 |
| 17 | Electrical Controllers Failed to receive or send feedbacks | 15 |
| 18 | Failure of gear train | 60 |
| 19 | Bearing Failures | 60 |
| 20 | Failure of Electrical system (Misalignment, Imbalance, looseness) | 40 |

Above details of time spend is for single failure only, shows that recovering time for hydraulic system, electrical system, bearing, gear train & pneumatic system are more compared to the others hence here to prevent the failure of these components are more concentrated & analyzed, The percentage wise details of recovering time has been shown by the pie chart to closely study the percentagewise occurrence of breakdown.

Fig. 2. Time Spend for Recover Breakdown

From the data time required to recover the failure in Hydraulic, pneumatic, gear train & electrical systems are maximum, thus these system & its associated failure need to find out and setting the proper preventive maintenance schedule to avoid the failure of these is important. Hydraulic & pneumatic system mainly having the same type of components like control elements, conveying components (pipes, hoses), filter, except the power source, Fig. 2 gives the percentages of time spend for different breakdown maintenance. The failure of electrical system (11%) accounts for the major time loss of production. bearing failure (8%) and failure of gear train (8%) also accounts for a considerable loss of production for the industry. Hence in this work contains the detail analysis of this system by FMEA.

Design FMEA is to identify the known failure modes and then ranking failures according to the relative impact on the product.

FAILURE MODE & EFFECT ANALYSIS (FMEA)

The objective of Process FMEA is to improve the existing process and find out how it can affect the system, environment and human. A product is considered to be failed when it does not give desired result or when it malfunctions in some way. It is not necessary that failures can happen only because of design or process failure but also can happen because of the operator error.

FMEA is to eliminate the root cause effect of any failure so as to improve the process and make ensure 100% customer satisfaction.

Process. FMEA is an effort to prevent failures due to process before they happen so as to assess the risk associated with that failure mode, to rank the issues in terms of severity, occurrence and detection and hence find the alternative measures to prevent the failure.

Process FMEA considers five main elements of the process namely: People, Materials, Equipment, Methods and Environment.

Design FMEA: Analyses a new process, product or service design before rollout to understand how it could fail once released. Exposes problems that may result in safety hazards, defects in product or service production processes.

Process FMEA: Used to improve existing transactional and operational processes to understand how people, materials, equipment, methods and environment cause process problems.

System FMEA: Analyses systems and subsystems in the early stage of concepts and design.

Table-3- Phases of FMEA

| Phase | Question | Output |
| --- | --- | --- |
| Identify | What can go wrong? | Failure cause and effect |
| Analyse | What is the number failure has occurred and what are the consequences | Risk Priority Evaluation= (severity*occurrence*detection) |
| Act | What can be done to eliminate the failure | Design solution, make plans, etc. |

Table-4- FMEA Chart for Hydraulic & Pneumatic System

| Components | Potential Failure Mode | Potential Failure Effects | Potential Causes | Action recommended | Action Taken |
| --- | --- | --- | --- | --- | --- |
| Directional Control Valve – Solenoid operated, 4/2, 3/2 type, forward & backward movement of it allows compressed air/pressurized oil go into the way (5/2 in case of pneumatic) | Failed to allow compressed air/ pressurized oil to go into the way of the valve or amount of suction & compression goes down. | There is no movement in the directional control valve and the leakage of air/oil | Pressure outside parameter | Replace dirty filters, clogged inlet line | Replacement |
|  |  |  | Incorrect assembly during maintenance | Check all the connections from the start | Repair the faulty part |
|  |  |  | Water in the air/oil supply line | Check Filter, Regulator, Lubrication | Repair the FRL unit |
|  |  |  | Wear of part | Replacement | Replacement |
|  |  |  | No signal/No gas supply | Replacement | Hose replaced |
|  |  |  | Spring problem | Check there is no leakage in the system | Replacement of the spring |
|  |  |  | Leakage | Replacement | Replacement |
|  |  |  | Crack in housing | Replace or Repair | Repair |
| Flow Control Valves-It influence the volume of the flow of compressed air/pressurized oil in both the direction | Unable to sense the volume of compressed air/pressurized oil to be send to the airway | There is malfunctioning/no movement of the valve | Pressure outside parameter | 1.Replace dirty filters, clogged inlet line \ 2.Tighten leaky connection | Replacement |
|  |  |  | Diaphragm failure | Check there should be no crack in the diaphragm | Replacement of the diaphragm |
|  |  |  | Mechanical failure | Check the spring/ball in minute detail | Replacement of the spring |
|  |  |  | Incorrect assembly during maintenance | Check all the connections from the start | Repair the faulty part |
|  |  |  | Water in the air/oil supply line | Check Filter, Regulator, Lubrication | Repair the FRL unit |
|  |  |  | Wear in parts No signal/No gas, supply | Replacement | Replacement |
|  |  |  | No signal/No gas supply | Check there is no leakage in the system | Hose replaced |
|  |  |  | Cracking of housing | Replace or Repair | Replacement |
|  |  |  | Pressure failure | Replace dirty filters, clogged inlet line | Cleaning of inlet line |
| Tubing/Hoses- It is used to transport the compressed air/pressurized oil to the desired destination | Compressed air/ pressurized oil is unable to reach its desired destination | Insufficient/Excessive pressure | Bending | Replacement | Replacement |
|  |  |  | Clogging (Blocking) | 1.Clean clogged inlet line 2.Change system fluid | Cleaning of inlet line |
|  |  |  | Leakage | Tubing material ruptured | Replacement |
|  |  |  | Fault in connection | Replace or repair | Replacement |
| Pressure Regulators- It reduces a high input pressure to a low working pressure and provides a steady output, despite changes in the input pressure | Failed to maintain the range of pressure required for the operation | Insufficient/Excessive pressure | Diaphragm failure | Replacement | Replaced |
|  |  |  | Leakage | 1.Check the hose and pipe 2.Replace or Repair | Replacement |
|  |  |  | Intake/Exhaust port failure | 1.Replace dirty filters, clogged inlet line 2.Tighten leaky connection | Leaky inlet connections tightened |
|  |  |  | Pressure switch not working | Replacement | Replaced |
|  |  |  | Cable connector | Mechanical failure- broken or damaged connector | Cable connector repaired |
|  |  |  | Electrical power failure | Check the electrical panel for proper connections | Electrical connections are corrected |
| Tubing/Hoses- It is used to transport the compressed air to the desired destination | Compressed air/pressurized oil is unable to reach its desired destination | Insufficient/Excessive pressure | Bending | Replacement | Replacement |
|  |  |  | Clogging (Blocking) | 1.Clean clogged inlet line 2.Change system fluid | Cleaning of inlet line |
|  |  |  | Leakage | Tubing material ruptured | Replacement |
|  |  |  | Fault in connection | Replace or repair | Replacement |
| Filters- It removes moisture and debris | Contamination problem is encountered | Icing or freezing of the exhaust air, causing the pump to cycle erratically | Water in the compressed air/pressurized oil supply | Check FRL (Filter, Regulator and Lubrication unit) | Replacement |
|  |  |  | Lockout valve failure | Mechanical failure-handle jammed | Replacement |
|  |  |  | Clogging | Clean the pores | Replacement |
| Lubricators- It injection oil mist to help lubricate the moving parts of the system | Insufficient oil in the system | Difficulty in operation of moving parts | Clogging/ Blocking | 1.Clean clogged inlet line | System fluid changed |
|  |  |  | Duct blocked | Cleaning | Replacement of ducts |
|  |  |  | Contamination | Cleaning | Cleaning |
| Reservoirs - It stores the compressed air. | Failed to store the compressed air | Insufficient/Excessive pressure | Cracking of housing | Replace or Repair | Replacement |
|  |  |  | External leak in the system | Tighten leaky inlet connection | Leaky inlet connections tightened |
| Electric controllers- it used to monitor a process condition in a machine and according give feedback | Failed to receive or send feedback for the closing and opening of switch | The operation of control valve is incomplete | Electrical power failure | Check the electrical panel for proper connections | Connections corrected |
|  |  |  | Proximity sensor failure | Component failure inside proximity senor | Sensor Replaced |
|  |  |  | PLC failure | Check the wiring of PLC | Snubber circuit can be used |

Detailed analysis of component with causes of failure, their effects & action to be taken has been done to reduce its breakdown rates, and this activity will alert the operator or maintenance personnel  to what, how & where the maintenance activity is to be perform. Accordingly a preventive maintenance schedule can easily planned as well as training to operator & daily maintenance plan also can designed. In this work according to the breakdown a preventive maintenance schedule is herewith designed which includes the daily, weekly, half yearly, & yearly pattern of maintenance.

PREVENTIVE MAINTENANCE

The most important reason for a PM program is reduced costs as seen in the following ways:

- Reduced production downtime, resulting in fewer Machine breakdowns.

- Better conservation of assets and increased life expectancy of assets, thereby eliminating premature replacement of machinery and equipment.

- Reduced overtime costs and more economical use of maintenance workers due to working on a scheduled basis instead of a crash basis to repair breakdowns.

- Timely, routine repairs circumvent fewer large-scale repairs.

- Reduced cost of repairs by reducing secondary failures. When parts fail in service, they usually

Damage the other parts.

- Reduced product rejects, rework and scrap due to better overall equipment condition.

- Identification of equipment with excessive Maintenance costs, indicating the need for corrective maintenance, operator training, or replacement of obsolete equipment.

- Improved safety and quality conditions.

Table-5- Preventive Maintenance Activity

| Sr. No | Problem | Correction Action/cause | Preventive Action |
| --- | --- | --- | --- |
| 1 | Disturbances in Sensor setting | Relocate the sensor, calibration status need to be checked, clean it | Daily checking for proper installation, cleaning |
| 2 | Handle pressure down in manual bending machine | Checked for looseness & pneumatic pressure & set back | Tightening & greasing, oiling the moving parts |
| 3 | Lower the Pneumatic pressure in various components (Air tank, FRL, Valve & Conveying line) | Removed the contamination, Looseness, recovered the leakages | Proper filtration, sealing & cooling system to maintain |
| 4 | Lower Clamping Pressure | Checked for looseness & pneumatic pressure & set back | Tightening & greasing, oiling the moving parts |
| 5 | Cutting length variation in CTL machine | Tighten the shaft with key & roller | Daily inspection for looseness required & set |
| 6 | Oil leakage through guider | Wear rate minimized by proper lubrication | Oiling level to maintain |
| 7 | Guider Screw not working as required in CTL machine | Handling was poor, made it automat | Visual inspection |
| 8 | Strippers becomes loose | Extra pressure & fluctuation | Avoid the pressure fluctuation |
| 9 | Stoppers not properly working | Sensor problem recovered | Cleaning & checked for detection power |
| 10 | Cutter wear down earlier in CTL machine | Poor lubrication | recovered |
| 11 | Clamping/decamping Pedal not working | Blockage at hinge, jammed the air | Uncovered the enclosed parts |
| 12 | Failure of hydraulic system components (DCV, PCV, FCV etc.) | Leakages, contamination, heat, & water droplets | Set the filter for proper meshing, wear, scratches |
| 13 | Spindle Speed goes down | Remedial for misalignment | Replacement of worn parts |
| 14 | Failure of Limit switch | Loose connection | Replacement |
| 15 | Contamination in Filter | Sealing agents proper | Replacement |
| 16 | Power Fluctuations | Connection problem | Daily visual inspection needs |
| 17 | Sealing agents wear, stretched or get loosed | Replaced | Replaced is done |
| 18 | Oil Leakages through components of hydraulic systems (hoses, pump, valve etc. | Sealing failure, contamination, wear | Replacement ,proper fittings |
| 19 | Belt slippage, cracked, frayed, glazed or showing the sign of wear | Replaced | Replaced is done |
| 20 | Electrical Controllers Failed to receive or send feedbacks | Checking for connection | Daily to be inspected |
| 21 | Failure of gear train | Misalignment, wear, lubrication | Need to done & inspect weekly |
| 22 | Bearing Failures | Misalignment, wear, lubrication | Need to done & inspect weekly |
| 23 | Failure of Electrical motor (Misalignment, Imbalance, looseness, winding burnt etc.) | Power fluctuation, installed properly | Tightening & well setting is required |

As per the requirement & minimize breakdown maintenance care should be taken that, components not fails during operation, hence the concept of preventive maintenance is important. To avoid this, before taking the Charge/starting machine a proper preventive maintenance activities should be performed, so that, actual status of every components before failure can be known.

Most of failure comes by not cleaning, not regular inspection, no proper or on time lubrication/greasing, heat generation, misalignment, looseness, therefore a preventive maintenance is required & it is suggested for the worked industry as follows, it is designed as per the failure causes observed in the machines & its equipment’s.

Table-6- Preventive Maintenance Checklist

| Sr. No. | Activity | Frequency |
| --- | --- | --- |
| 1 | Check cleanliness of machine | Daily |
| 2 | Check the slide lubrication oil level | Daily |
| 3 | Check the slide lubrication | Daily |
| 4 | Check the hydraulic oil leakage in the pipe line | Daily |
| 5 | Pneumatic pressure 4 to 7 kg/cm2 | Daily |
| 6 | Check the main motor terminal | Weekly |
| 7 | Check press oil level | Daily |
| 8 | Check automation oil level | Daily |
| 9 | Handle pneumatic pressure & misalignment in parts | Weekly |
| 10 | Sensor installation setting | Daily |
| 11 | Clamping Pressure & it’s setting | weekly |
| 12 | Check of Guider screw setting | Daily |
| 13 | Checking stripper misalignment | Weekly |
| 14 | Check wear of cutter | Daily |
| 15 | Contamination of filter | Weekly |
| 16 | Pneumatic pressure at conveying lines & connectors | Weekly |
| 17 | Belt looseness, slippage | Weekly |
| 18 | Electrical motor coil burnt, misalignment | Weekly |
| 19 | Cleaning of Pedal assembly, filter | Weekly |
| 20 | Checking Bearing for all associated components looseness, cleaning | Weekly |
| 21 | Cleaning of machine compartment & spindle | Weekly |
| 22 | Checking installed tool wear & tear | Daily |
| 23 | Checking of cooling system to heat generation | Daily |
| 24 | Checking speed of spindle | Weekly |
| 25 | Check Control elements to all inlet & outlet lines | Weekly |
| 26 | Aware the operator to all these activity | Daily |
| 27 | Training to all workers | Half yearly |

CONCLUSION

In this work all repeated breakdowns were Analyzed along with the critical parts, which has been under breakdown condition is also identified and analyzed. The reason for the breakdown has been analyzed by The RCM techniques and methods, the root causes of the breakdowns were identified. This in turn helped to develop and improve a new preventive maintenance checklist for the machine. This method is used to prevent the failure of equipment before it actually occurs. The average availability of critical machine after root because analysis & followed of preventive maintenance schedule is increased.

After root cause analysis there is an improvement in the maximization of planned productivity. This is because of proper diagnosis of the existing system and by employing proper preventive maintenance schedule. Therefore whenever a breakdown occurs, the root cause of the breakdown has to be identified. Then some efforts should be made to improve this system using preventing maintenance and counter measures, such that similar type of breakdown can be reduced.

REFERENCES

- Katharina Fischer,, Francois Besnard, and Lina Birling, “Reliability-Centred Maintenance for Wind Turbines Based on Statistical Analysis and Practical Experience”IEEE Transactions on Energy Conversion, vol.PP, no.99, pp.1-12.

- Marvin Rausand, “Reliability centered maintenance” Reliability Engineering and System Safety 60 (1998) 12 I – 132, pp 121-131.

- Islam H. Afefy,”Reliability-Centered Maintenance Methodology and Application: A Case Study”, scientific research engineering, 2010, 2, pp 867-873.

- Li, C. H., & Chang, S. C. (2002). “Model for preventive maintenance Operations and forecast method for interval triggers” Semiconductor Manufacturing Technology workshop 2002, 10–11 Dec. 2002, and pp. 275–277.

- Pan E, Liao W, Xi L (2010) “Single-machine-based production scheduling model integrated preventive maintenance planning” Int. J. Adv Manuf. Technology 50(1–4):365–375.

- Akturk, M.S. and Avci, S., “Tool allocation and machining conditions- based preventive maintenance for CNC machines” Eur. J. Oper. Res., 1996, 94, 335–348.

- Kiran M, Cijo Mathew, Jacob Kuriakose (2013), “Root Cause Analysis for Reducing Breakdowns in a Manufacturing Industry” International Journal of Emerging Technology and Advance Engineering, Vol.3, Issue 1, 2013, pp. 211-216.

- O.E. Simolowo, M.Phil.  and M.B. Adeniji, (2009), “The Effect of Tribological Processes on Productivity: A Case Study of Industries in Ibadan Metropolis of Nigeria.” The Pacific Journal of Science and Technology, 1 November, 2009, vol. 10, pp 372-381.

- R.S.Mhetre, R.J.Dhake,”Using Failure Mode Effect Analysis in a Precision Sheet Metal Parts Manufacturing Company”, Int. Journal of Applied Sciences and Engineering Research, Vol. 1, No. 2, 2012, pp 302-311.

- A. H. Gomaa, “Maintenance Planning and Management,” A Literature Study, American University in Cairo, Cairo, 2003.

- M.C. Eti a, S.O.T. Ogaji b, S.D. Probert b, “Reducing the cost of preventive maintenance (PM) through adopting a proactive reliability-focused culture”,(2006) Published by Elsevier Ltd. applied energy,83, pp 1235-1248.

- Lawrence P. Chao, Kosuke Ishii, “Design Process Error Proofing: Failure Modes and Effects Analysis of the Design Process”, Journal of Mechanical Design, MAY 2007, Vol. 129, pp 491-501.